## Slide 1
Arista ATD with Ansible Tower

## Slide 2: Network to Code Services Offerings
Workflow Automation & Optimization
Software Development
Training / Workshops
Review Network Operations Workflows
Python for Network Engineers
DevOps Tools
Network Device APIs
Private/Public Courses
Custom network Applications
DevOps Tool Plug-Ins & Integrations
Helps Eliminate repetitive tasks
Optimize
Drive Down operational inefficiencies
Bootcamps
Ansible for Network Engineers

## Slide 3: Win a FREE Network Automation Book!
Drop off a business card
Have the chance to win Network Programmability and Automation

## Slide 4: Arista ATD Integration Components

## Slide 5: Leaf - Spine Topology
eBGP used both within the underlay and overlay
iBGP between MLAG peers
Hosts are dual connected
  Host 1 in Vlan13
  Host 2 in Vlan12
  Host 3 in Vlan13
  Host 4 in Vlan12
Looking for Layer2 reachability across VXLAN/EVPN fabric
eBGP
100.1.11.0/30
.1
.2
eBGP
100.2.11.0/30
iBGP
VARP
MLAG
Host1
- Vlan 13
- 10.11.13.11/24
AS
101.0
AS
101.1
AS
101.2
Host2
- Vlan 12
- 10.11.12.12/24
Host3
- Vlan 13
- 10.11.13.13/24
Host4
- Vlan 12
- 10.11.12.14/24

## Slide 6: Scope of work
Start with a default configuration on our Arista switches
Validate that the Linux servers cannot reach their default gateway
One-Click build our entire underlay and overlay with Ansible
  Build each device’s configuration section-by-section, assemble, and push
Validate that the Linux servers can reach their default gateway
Showcase a working EVPN fabric where host 2 can ping host 4
  Layer 2 adjacency across a VXLAN tunnel
Add a new VLAN to the EVPN fabric with a targeted playbook
Validate that host 1 can now ping host 3

## Slide 7: Use cases for Ansible Tower
Integrations with CVP, ServiceNow, Slack and NetBox
Validate network compliance of state and configuration
Obtain real-time facts from network devices or CVP
Configure multi-vendor environments
Copy / Install / Upgrade network OS across your network
Integrate dynamic inventory with CVP, Netbox, etc.
Add network devices to monitoring solutions
Real-time notification of configuration changes

## Slide 8: github.com/networktocode/arista-atd

## Slide 9: Network to Code At A Glance
WHAT WE DO
Network to Code provides high value services, training, and development in the network programmability and automation space.
WE BRIDGE THE GAP BETWEEN DEVOPS AND NETWORK ENGINEERING